## Slide 1
AIQM GROWTH MONITOR
Option B: Local Deployment
on Bulbasaur
Closed-loop autonomous MBE growth via RHEED classification,
RL temperature policy, and PID-controlled OWON power supply
Yang Lab / Meng Group Collaboration
Meeting — March 6, 2026

## Slide 2
Two Operating Modes for MBE Growth
The system supports switching between human-driven and autonomous operation.
NORMAL MODE
Human-Driven Growth
Standard lab PSU (not programmable)
RHEED on kSA screen, pyrometer on TemperaSure
Human watches patterns, adjusts temperature
Our system is not required
AI-SCIENTIST MODE
Closed-Loop Autonomous
OWON PSU swapped in (programmable, serial)
RHEED frames streamed to Classifier2 ML
RL policy decides temperature adjustments
PID loop drives OWON, human can override
OUR SYSTEM

## Slide 3
Why Run Everything on the Lab PC?
AI-Scientist mode requires direct access to three hardware interfaces on the same machine.
OWON PSU
USB Serial
PID voltage control
to substrate heater
Pyrometer
COM4 / Modbus RTU
Temperature feedback
for RL + PID loop
RHEED Camera
kSA Screen Grab
Frame capture with
exact false-color LUT
Conclusion: All three interfaces are physically connected to Bulbasaur. No remote architecture can control the OWON PSU or read COM4 directly. The GUI must run on the lab PC.
Rejected: TeamViewer screen grab (lossy, high latency), Frame Server (still needs Python + can't control PSU), Direct GigE (conflicts with kSA)

## Slide 4
Hardware Topology — Bulbasaur
BULBASAUR — MBE Lab PC (Windows)
kSA 400
RHEED display — window: "AVT Manta_G Live Video"
TemperaSure 5.7
Pyrometer GUI — BASF TemperaSure 5.7.0.4
COM4 (PL2303GS)
RS-422 to BASF Exactus pyrometer via IFD-5
GigE
Allied Vision Manta G-033B (656x492, mono, 12-bit)
OWON PSU
USB serial — swapped in for AI-Scientist mode
Python + GUI
To be installed — Growth Monitor + Classifier2 + PID
DEV MAC
Train models (MPS GPU)
Develop GUI + drivers
Copy artifacts to Bulbasaur
Deploy: model + code
via USB drive or network
IP: 205.208.25.122 (campus) — Remote: TeamViewer only (monitoring, not control)

## Slide 5
What We've Built So Far
SOFTWARE (DONE)
Driver ABCs (camera, pyrometer) + 3 implementations each
GUI tabs: RHEED, Pyrometer, PSU, Thermocouple, Dashboard
Growth Monitor dashboard with human classification sliders
Tier 1 auto-capture (intensity change detection)
Tier 3 auto-capture (classification JS-divergence)
ClassifierBridge — loads Classifier2, expose classify(frame)
Session logging (sensor CSV, commit CSV, frame PNGs)
GrowthApp orchestrator (ARM/DISARM/START/STOP)
CLASSIFIER2 (TRAINED)
100% ideal-split accuracy (30/30)
88.3% pairwise holdout (159 ideal images)
5 classes: (1x1), Tw(2x1), c(6x2), rt13, HTR
CPU inference: ~80 ms/frame (ResNet18, 11.3M params)
BLOCKERS
Python not installed on Bulbasaur
RHEED gun down — no live camera testing
Pyrometer was off during last visit

## Slide 6
AI-Scientist Mode: Full Closed-Loop
~120 ms per cycle | 1 FPS target | All local on Bulbasaur
RHEED
Screen Grab
~10 ms
Classifier2
Inference
~80 ms
RL
Policy
~1 ms
PID
Controller
~1 ms
OWON
PSU Write
~10 ms
FEEDBACK LOOPS
Pyrometer (COM4)
Modbus RTU, ~20 ms read
Temperature feedback to RL + PID
OWON PSU (USB)
Serial write, ~10 ms
Voltage to substrate heater
Auto-Capture
Tier 1/2/3 detectors
Log frames + CSVs to session folder
Growth Monitor GUI
Human override at any time
AI confidence bar, classification, BAD indicator

## Slide 7
ML Classification Pipeline
kSA Frame
(656x492 RGB)
False-color LUT
Resize
224x224
Normalize
SimCLR
ResNet18
Encoder (512-dim)
Reward
Head
512 > 256 > 5
Win-Rate
Classify
vs 159 ideal refs
OUTPUT
predicted_class
Argmax of 5 win-rates
e.g. "c(6x2)"
classification_scores
5 probabilities
(1x1, Tw, c6x2, rt13, HTR)
is_bad + bad_confidence
Compared against 18
bad reference images
quality
0-1 scalar,
overall surface quality
Training data: Bradley-Terry reward model trained on 678 pairwise human comparisons + 159 ideal images across 5 reconstruction types. Model was trained on kSA false-color screenshots — screen grab on Bulbasaur produces exact match to training distribution.

## Slide 8
Performance Budget — 1 FPS Closed Loop
Total loop: ~120 ms per cycle on CPU. Target: 1 frame per second (plenty of headroom).
Screen
Grab
10 ms
Modbus
Read
20 ms
Classifier2
Inference
80 ms
RL
Policy
1 ms
PID +
Serial
11 ms
Install Footprint on Bulbasaur
Python 3.12
~30 MB
User-level install (winget / embeddable zip)
PyTorch CPU-only
~150 MB
No CUDA/MPS needed
PyQt6 + deps
~100 MB
GUI framework
Model artifacts
~50 MB
best_model.pth + ideal reference images
Total: ~350 MB

## Slide 9
Deployment Plan — Next Steps
01
Get permission to install Python on Bulbasaur
User-level install via winget, MS Store, or embeddable zip (no admin needed)
02
Clone AIQM repo + copy model artifacts
Via git or USB drive. Include best_model.pth and 159 ideal reference images
03
pip install dependencies
PyQt6, torch (CPU-only), pymodbus, mss, pillow, numpy — all pure pip
04
Connect OWON PSU via USB
Verify serial port detection and PID loop on Bulbasaur
05
Test pyrometer serial (COM4)
Modbus RTU read when pyrometer is powered on — driver already written
06
Test kSA screen grab
Verify ScreenGrabCamera captures RHEED window natively at full resolution
07
Full integration test
Live RHEED + pyrometer + Classifier2 + OWON PID + auto-capture logging
Key blocker: Step 01 — everything else is ready to go once Python is on Bulbasaur.

## Slide 10
Summary
1. Two modes: Normal (human) and AI-Scientist (closed-loop autonomous)
2. Option B is the only viable architecture — all hardware is on Bulbasaur
3. Software is built and Classifier2 is trained (100% ideal-split accuracy)
4. Full loop budget: ~120 ms/cycle, well within 1 FPS target
5. One blocker: permission to install Python on Bulbasaur (~350 MB)
Yang Lab / Meng Group | March 2026